## Slide 1: Data Analytics Framework for A Game-based Rehabilitation System
Jiongqian (Albert) Liang*, David Fuhry*, David Maung*, Alexandra Borstad+, Roger Crawfis*, Lynne Gauthier+, Arnab Nandi*, Srinivasan Parthasarathy*
* Department of Computer Science and Engineering.
+ Wexner Medical Center.
The Ohio State University

## Slide 2: Outline
Motivation
Introduction
Data Analysis Framework
Experiments
Conclusion

## Slide 3: Motivation
Stroke happens when blood flow to an area of the brain stops.
Around 4 million stroke patients in the US.
It costs the US more than $34 billion annually.

## Slide 4: Motivation

## Slide 5: Motivation
Getting physical therapy is difficult.
Fewer than 1% receive it (in the US):
  Too costly
  Travelling difficulties for stroke patients
  Not enough providers

## Slide 6: Motivation

## Slide 7: Motivation
See full video at https://youtu.be/G5MyBNvNEfg

## Slide 8: Introduction
Patients play the game in front of Kinect.
Kinect-based Rehabilitation Game
Data Analytics Framework
Evaluation of the rehabilitation & Feedback
Skeleton Data
Game Log
Kinect collects skeleton data. Software recognizes gesture (game log).
Data analytics for performance evaluation.

## Slide 9
In this work, we
  Propose a data analytics framework to evaluate the efficacy of the rehabilitation.
  Show some preliminary results based on some participants we recruited.
  Show our evaluation based on game data is consistent with a standard test in the lab.
Introduction

## Slide 10: Data Analytics framework
Data Preprocessing
Rehabilitation Analysis
Hand Speed
Angle Speed
Gesture Segmentation
Temporal smoothing
Anomaly filtering
Contextual Filtering
Region Segmentation
Trend Analysis
Range of Motion

## Slide 11: Data Preprocessing
1. Temporal smoothing:
Problem: limited sensor spatial resolution, but 30 snapshots each sec. Movement might be due to “jitter” and sensor limitations.
Solution: set a sliding time window T (200 ms), and average snapshots.
Data Preprocessing
Rehabilitation Analysis
Contextual Filtering

## Slide 12: Data Preprocessing
2. Anomaly filtering:
Problem: there are some erroneous snapshots.
Solution: Inside a time window, remove snapshot if the distance of it to the averaged snapshot > µ+3𝞂.
Data Preprocessing
Rehabilitation Analysis
Contextual Filtering

## Slide 13: Contextual Filtering
Gesture Segmentation:
Reason: there are different gestures. Analyze patients’ movement during each gesture period (dynamically).
Solution: concatenate continuous snapshots of the same gesture with temporal gaps smaller than 2,000 ms (using game log).
Data Preprocessing
Rehabilitation Analysis
Contextual Filtering

## Slide 14: Contextual Filtering
Region Segmentation:
Reason: the game contains several different regions with different difficulties and intensities.
  Self-paced movement: e.g., Rowing.
  Fast-paced movement: e.g., Rapids.
Solution: refer to the game log, synchronize the timestamp and segment out skeleton data.
Data Preprocessing
Rehabilitation Analysis
Contextual Filtering

## Slide 15: Rehabilitation analysis
Hand speed: movement speed of hand.
Data Preprocessing
Rehabilitation Analysis
Contextual Filtering
dis
Distance =
at
at
Time=()

## Slide 16: Rehabilitation analysis
Angle speed: similar to movement speed, but on angle.
Data Preprocessing
Rehabilitation Analysis
Contextual Filtering
Angle distance.

## Slide 17: Rehabilitation analysis
Range of Motion: difference between min and max angles of a body joint. It measures the active range.
Data Preprocessing
Rehabilitation Analysis
Contextual Filtering
max
min

## Slide 18: Experiment Analysis
8 participants were recruited (at least 3 months post-stroke)
Participant ID | Affected Side | Days | Total Mins | Avg mins/day
P1 | Left | 21 | 678.6 | 32.3
P2 | Right | 14 | 803.2 | 57.4
P3 | Left | 19 | 656 | 34.5
P4 | Right | 21 | 978.5 | 46.6
P5 | Right | 20 | 2185.5 | 109.3
P6 | Right | 21 | 2084.3 | 99.3
P7 | Right | 20 | 1351.4 | 67.6
P8 | Right | 13 | 881.6 | 67.8

## Slide 19: Experiment Analysis
Pre/post comparison: before and after the participants used the rehab system, they conduct Wolf Motor Function Test (WMFT).
The test measures the time to perform 15 standardized motor tasks.
Examples: lifting pencil and placing the hand on top of a box.
Calculate the rate based on the time.

## Slide 20: Experiment Analysis: three parts
Two-half Comparison
Region Segment
Trend Analysis

## Slide 21
Two-half comparison approach:
  Divided the whole rehabilitation period into two halves.
  Calculate the kinematic variables in these two divisions respectively (hand speed, angle speed, etc.).
  Compare the averaged values of two halves.
  Conduct t-test to see the significance of difference.
Compare with WMFT result.
Two-half Comparison
Region Segment
Trend Analysis
Experiment Analysis

## Slide 22
Observation 1: Improvements over the two halves.
Experiment Analysis
Two-half Comparison
Region Segment
Trend Analysis

## Slide 23
Wolf Motor Function Test result
Observation 2: consistency. Trend & Scale.
Experiment Analysis
Two-half Comparison
Region Segment
Trend Analysis

## Slide 24
Two-half comparison & Wolf Motor Function Test:
  Very different metrics (game data analysis vs. lab test).
  Show very consistent pattern of performance.
  Kinematic measurement based on game data can serve as complimentary assessment (cheaper, more convenient).
Experiment Analysis
Two-half Comparison
Region Segment
Trend Analysis

## Slide 25
Self-paced (Rowing Region) vs. fast-paced (Rapids Region) *.
Experiment Analysis
Two-half Comparison
Region Segment
Trend Analysis
* P1 did not have different
regions during gameplay.
?

## Slide 26
Two-half Comparison
Region Segment
Trend Analysis
Conduct a fine-grained trend analysis:
  Segment the game data by game session.
  Compute the average hand speed every five minutes each session.
Experiment Analysis
Inverted “U”: sign of fatigue.

## Slide 27
Model inverted ‘U’ as a quadratic function (quadratic regression).
Compute the ratio of inverted ‘U’ shape:
Experiment Analysis
Two-half Comparison
Region Segment
Trend Analysis

## Slide 28
More gameplay time  More inverted “U”
<
Pearson correlation
coefficient:
Two-half Comparison
Region Segment
Trend Analysis

## Slide 29: Conclusion
Propose a data analytics framework to evaluate game-based rehab.
Patients have obvious improvement but in different aspects. Consistent with standard WMFT in the lab.
Reveal sign of fatigue, correlated with the gameplay time.

## Slide 30: Questions?
Acknowledgements:
PCORI, UL1TR001070, NSF-EAR-1520870 and NSF-DMS-1418265.